## Slide 1
RTOS-Based Smart Health Monitoring System with Fall Detection
Name: Himani Deore
Roll No: 312044 | PRN: 22311497
Class: TY B ENTC

## Slide 2
Project Abstract
In health monitoring systems, it is important to continuously track vital parameters such as heart rate and oxygen saturation, and detect emergency conditions like falls. However, many basic embedded systems are not able to handle multiple operations simultaneously, leading to delayed response and unreliable monitoring.
There is a need for a system that can monitor multiple parameters in real time, respond quickly to abnormal conditions, and provide immediate alerts for improved safety.
This embedded system implements a real-time health monitoring solution using FreeRTOS for concurrent task management. The system integrates vital sign monitoring with intelligent fall detection, providing immediate alerts through an interrupt-driven touch interface.
FreeRTOS-Based Multitasking
Priority-based scheduling for concurrent sensor monitoring
MAX30100 Sensor Integration
Heart rate and blood oxygen saturation measurement
MPU6050 Fall Detection
Accelerometer-based impact and free-fall analysis
Interrupt-Driven Control
Fast response touch sensor with semaphore synchronization

## Slide 3
Project Objectives
The system aims to provide continuous health monitoring with immediate fall detection capabilities for elderly care applications.
Design and configure multiple concurrent tasks with appropriate priorities and stack sizes
To interface the MAX30100 sensor with STM32 using I2C for real-time acquisition of heart rate and SpO₂ data
Implement BPM calculation using peak detection algorithm
Detect fall using MPU6050 with threshold-based logic.
Implement interrupt-based touch control (EXTI)
Use mutex for safe I2C communication and Display real-time data on LCD

## Slide 4
Hardware Components
The system comprises a microcontroller platform with integrated sensors and display modules for comprehensive health monitoring.
STM32 Microcontroller
ARM Cortex-M core running at 72 MHz, providing sufficient processing power for real-time operations
MAX30100 Sensor
Integrated pulse oximeter and heart-rate monitor using photoplethysmography (PPG) principle
MPU6050 Sensor
3-axis accelerometer and gyroscope for motion detection and fall analysis
Capacitive Touch Sensor
Interrupt-generating touch button for user interaction and system control
16×2 LCD Display
Character LCD for real-time data visualization and system status updates

## Slide 5
System Design: FreeRTOS Architecture
The system is implemented using FreeRTOS with four concurrent tasks assigned different priorities to ensure efficient execution and fast response to critical events.
01
Touch Control Task (Priority 3)
Handles user input using EXTI interrupt and controls system ON/OFF state transitions.
(Highest priority for immediate user response)
02
MAX30100 Task (Priority 1)
Reads heart rate and SpO₂ data periodically (~100 ms) and performs basic signal processing and averaging.
(Normal priority as slight delay is acceptable)
03
MPU6050 Task (Priority 2)
Continuously monitors accelerometer data and detects fall conditions using threshold-based logic.
(Higher priority due to critical nature of fall detection)
04
Display Task (Priority 0)
Updates LCD with latest sensor readings and system status at regular intervals (~500 ms).
(Lowest priority as it is not time-critical)

## Slide 6
Interrupt-Based Touch Control
The touch sensor is connected to a GPIO pin configured as an external interrupt (EXTI), allowing immediate detection of user input.
Working:
Touch input triggers EXTI interrupt on GPIO pin
Interrupt Service Routine (ISR) is executed instantly
System state (ON/OFF) is toggled inside task/logic
Eliminates need for continuous polling
Key Features:
Fast response to user input
Efficient CPU usage (no polling loop)
Simple and reliable control mechanism
Debounce handled using software delay

## Slide 7
Heart Rate & SpO₂ Measurement
The MAX30100 uses photoplethysmography (PPG) to measure blood volume changes by emitting infrared and red light through tissue.
Signal Acquisition
IR and Red LEDs emit light into tissue
Reflected light intensity varies with blood flow
Sensor provides digital IR and Red values via I2C
DC & AC Component Extraction
DC component → baseline signal (average value)
AC component → pulsatile part due to heartbeat
AC = signal - DC
Heart Rate Calculation
Peak detection applied on IR signal
Time difference between peaks → BPM
BPM = 60000 / Δt
Averaging used to stabilize readings
SpO₂ Calculation
Ratio of Red and IR signals is computed
R = (AC_red / DC_red) / (AC_ir / DC_ir)
SpO₂ estimated using empirical relation
SpO₂ ≈ 110 - 25 × R

## Slide 8
Fall Detection Logic
The MPU6050 monitors acceleration (Z-axis) and detects fall using threshold-based logic.
1
Acceleration drops below a threshold, indicating sudden downward motion.
|Az| < FALL_THRESHOLD_LOW
Represents near weightlessness during fall
2
Impact Detection
Acceleration increases sharply after free fall.
|Az| > FALL_THRESHOLD_HIGH
Indicates impact with groundds
3
Checks if there is no significant movement after impact.
Time delay after impact (NO_MOVEMENT_TIME)
Confirms actual fall condition

## Slide 9
Working Principle & Results
System Operation
When the system is powered ON:
FreeRTOS scheduler initializes and runs all tasks
MAX30100 task continuously reads HR & SpO₂ data
MPU6050 task monitors acceleration for fall detection
Touch interrupt controls system ON/OFF
Display task updates LCD with real-time values
If a fall or abnormal condition is detected, the system immediately updates the display with an alert.
Performance Observations
Real-time heart rate and SpO₂ values displayed
Stable readings achieved after signal filtering
Touch input responds instantly using EXTI interrupt
Fall detection triggered successfully based on motion
System operates smoothly with multitasking

## Slide 10
THANK YOU